## Slide 1
Application Of
Bilevel Programming To
Model Predictive Control
Subhi Gupta and Hari S. Ganesh
Discipline of Chemical Engineering,
Indian Institute of Technology Gandhinagar.
Background
Motivation
Results
Conclusion
Important Terminologies
) + ) +
) + ) +
) + ) +
Hierarchy is characterized by vertical decomposition, priority of action, and performance interdependence.
Bidirectional communication exists between levels in any hierarchical large-scale system.
Figure 1 shows the five levels in the process control hierarchy.
Figure 2 represents the simplest hierarchical system.
Figure 1: Process Control Hierarchy
Upper-level subsystem
Controller 1 (Optimisation Problem 1)
Figure 2: Bilevel decision-making structure
Lower-level subsystem
Controller 1 (Optimisation Problem 1)
Sparse attempts have been made to solve hierarchical control problems.
Multi-parametric bi-level programming algorithm have been used in the proposed work to solve bilevel multi-parametric/explicit MPC controller (Bilevel mp-MPC).
Use of a multi-parametric programming approach guarantees a global optimal solution for multilevel programming problems.
Methodology
System considered: Temperature Control Laboratory (TCLab)
Steps Taken:
  Modeling of the system.
  Model equations reduced to linear state-space equations.
  MPC and mp-MPC algorithms implemented on the system.
  Run-time operation compared (Table 1).
  Billevel MPC control structures designed.
  Solved using multi-parametric bi-level programming algorithm.
  Closed loop validation performed.
Results (Figure 6 and 7) show that designed controllers manage
to follow the temperature set-point.
Decision connections
Information
connections
No. | Type of MPC | Total runtime (s)
1 | Online MPC | 5.351
2 | mp-MPC | 0.912
Comparison based on runtime operation.
Runtime operation reduced by 83.52%.
Table 1
Bilevel MPC Control Structures
Bilevel MPC Control Structure
Inner Level solved multi-parametrically
The solution obtained after solving five LP outer level problem
Fields | Optimised variables () | Function values
1 | (0.5000 , 0.5000) | -6.00
2 | (0.5000 , 0.5000) | -6.00
3 | (0 , 0.7500) | -23.00
4 | (0.5000 ,0.5000) | -6.00
5 | (0,0.9000) | -26.00
Fields |  | Function values
1 | (0.5000 , 0.5000) | -6.00
2 | (0.5000 , 0.5000) | -6.00
3 | (0 , 0.7500) | -23.00
4 | (0.5000 ,0.5000) | -6.00
5 | (0,0.9000) | -26.00
Global optimum solution
Fields | Optimised variables (, ) | Function values
1 | (0,0,0) | 1.5
2 | (0,0,0) | 1.5
3 | (0.0.5,0) | 2
4 | (0,0,0) | 1.5
5 | (0,0.6,0.4) | 3.2
Fields |  | Function values
1 | (0,0,0) | 1.5
2 | (0,0,0) | 1.5
3 | (0.0.5,0) | 2
4 | (0,0,0) | 1.5
5 | (0,0.6,0.4) | 3.2
Substitution of optimized variables to get solutions to inner-level problems.
Five critical regions are obtained with y as an explicit function of x.
System Model
Constraints
Objective function
Multi-parametric Bilevel Programming Algorithm
Linear Model Predictive Control on TCLab
Multilevel Structure
The proposed work presented multi-parametric bilevel programming framework under uncertainty.