## Slide 1
CL-699 Mid-Semester Presentation
Subhi Gupta
Discipline of Chemical Engineering,
Indian Institute of Technology Gandhinagar,
Palaj, Gujarat – 382055
India
Bilevel Programming and its Application to
Model Predictive Control

## Slide 2
Content
Hierarchical order in process industry
Bilevel Programming Problem (BLPP)
Parametric Programming
Multiparametric Programming
Dual Heater Modeling of TCLab.
Bilevel Model Predictive Control
Model Predictive Control (MPC) formulation
Data-Driven State Space equations
Closed Simulation results
Conclusions and Future Work
Acknowledgement

## Slide 3
Hierarchical order in process industry
Background
Process control activities are organized in the form of hierarchy as shown in Figure 1.
For profitable plant operation the process control activities at different levels should be carefully coordinated.
Multi-level decision structures can be mathematically represented using multi-level programming principles.
Reference: Seborg DE, Edgar TF, Mellichamp DA, Doyle III FJ.2016 Sep 13.
Figure 1: Hierarchy of process control activities
To measure process variables and implement the calculated control actions.
Standard feedback and feedforward control techniques.
Model predictive control (MPC) strategy.

## Slide 4
Bilevel Programming Problem (BLPP)
In some literature, researchers have addressed bilevel decision-making problems.
Ryu et.al have taken one level as plant planning/control problem and other level as as distribution network problem.
Styliani et.al have recasted planning and scheduling integration as a bi-level multi-follower problem. Upper level (planning) and lower level (scheduling).
Bilevel programming have evolved significantly in recent years.
Tri-level and other general multi-level programming problems
too are evolving gradually.
Reference: Ryu JH, Dua V, Pistikopoulos EN. 2004 Jun 15;28(6-7):1121-9.
Reference: Avraamidou, S., & Pistikopoulos, E. N. (2018, June). IEEE.
Motivation

## Slide 5
Bilevel Programming Problem (BLPP)
Bilevel Optimization Model
Reference: Ryu JH, Dua V, Pistikopoulos EN. 2004 Jun 15
Leader’s problem or
High level decision problem
Follower’s problem or
Low level decision problem
First level (production model) is constrained by another optimization problem (second level,the distribution model).
Process configuration of an enterprise
Aim is to minimise both Production cost and distribution cost.

## Slide 6
Parametric Programming
Takes into account varying parameters (𝜃).
Approach is to obtain the optimal solution (𝒙) as an explicit function of the parameters.
General parametric nonlinear programming problem
An Effective Solution Strategy
Reference: Faísca NP, Dua V, Pistikopoulos EN. 2007 Feb 9;1:1-23.
Image Source: https://parametric.tamu.edu/POP/

## Slide 7
Multiparametric Programming
Formulation of Multiparametric Linear (mp-LP) and Quadratic Programming (mp-QP)
The parameter space(𝜃 ) is partitioned into nine set of critical regions (CRi).
Each critical region has its own function optimal solution x*(𝜃 ) and Z*(𝜃 )
Verification was done using quadprog solver
Solution of mp-QP: 𝒙(𝜃)𝘪=𝑊𝘪𝜃 + 𝘸 CR𝘪: Φ𝘪𝜃≤𝜙𝘪
Reference: Faísca NP, Dua V, Pistikopoulos EN. 2007 Feb 9;1:1-23.

## Slide 8
Bilevel Programming Problem (BLPP)
Formulation of Linear BLPP (LP/BLPP)
Inner Level solved multi-parametrically
Reference: Faísca, Nuno P., et al. Journal of Global Optimization 38.4 (2007).
Five critical regions are obtained with y as an explicit function of x.

## Slide 9
Bilevel Programming Problem (BLPP)
Solution of a linear bilevel programming problem.
Solution obtained after solving outer level problem
Fields | Optimised variables (𝑥) | Function values
1 | [0.5000 ; 0.5000] | -6
2 | [0.5000 ; 0.5000] | -6.0000
3 | [0 ; 0.7500] | -23.0000
4 | [0.5000 ; 0.5000] | -6.0000
5 | [0 ; 0.9000] | -26
Global optimum solution

## Slide 10
Bilevel Model predictive control
One of the application of Bilevel lies in hierarchical model Predictive control (MPC) structures.
In recent attempt has been made to solve MPC in hierarchical manner.
Styliani et.al in 2017 employed two level hierarchical mp-MPC on a continuous stirred tank reactor (CSTR) system.
Use of a multi-parametric bi-level algorithm for the development of explicit hierarchical controllers has limited application.
So such algorithms hold a good possibility to be explored and extended on more complex systems in near future.
Controller 1 (Optimisation Problem 1)
Controller 2 (Optimisation Problem 2)
System
Avraamidou S, Pistikopoulos EN.In Computer aided chemical engineering 2017 Jan 1.Elsevier.

## Slide 11
Model Predictive Control (MPC)
Basic Concept of Model Predictive Control
Reference 6: Seborg DE, Edgar TF, Mellichamp DA, Doyle III FJ.2016 Sep 13.
Current time instant

## Slide 12
Model Predictive Control (MPC) Formulation
MPC formulation is first reformulated into quadratic form using ss2qp_yalmip.
At each sampling instant the quadratic problem is solved using cplexqp solver.
quadprog can also be used but cplexqp gives more stable results.
State space equations

## Slide 13
Data Driven State Space Equations
The state space equations used as linear constraints in MPC formulation were to be obtained first.
The differential equations representing the physical system are first linearised using MATLAB System Identification ToolBox.
Step Response Analysis method was employed on TCLab, a two heater and two sensor device (MIMO system) .
State space equations were obtained from
MATLAB System Identification Toolbox

## Slide 14
Data Driven State Space Equations
Dual Heater Modeling of TCLab (MIMO System)
Two energy balance equations that describe the dynamic temperature response

## Slide 15
Data Driven State Space Equations
Dual Heater Modeling of TCLab (MIMO System)
Steady state achieved for Q1=30 and Q2=30
Steady state achieved for Q1=30 and Q2=30

## Slide 16
Data Driven State Space Equations
Dual Heater Modeling of TCLab (MIMO System)
Temperature simulation for step changes in Q1 and Q2
The above step response was used to develop data-driven state-space equations using System Identification Toolbox.
The resulting pseudo states equations obtained in matrix form were used as linear constraints in MPC formulation.

## Slide 17
Closed-loop Simulation results.
Demonstration of MPC Control Calculations & Design and Tuning of Parameters
Best Case of Tuning Parameters
Next Task
MPC formulation was solved multi-parametrically (mp-MPC).
The idea was to confirm that the solution obtained were identical with that of MPC technique.

## Slide 18
Closed Loop Simulation Results
Online MPC
mp-MPC
Online MPC and mp-MPC results match.

## Slide 19
Closed loop Simulation Results
Online MPC
mp-MPC
Online MPC and mp-MPC results match.

## Slide 20
Closed Loop Simulation Results
Online MPC
mp-MPC
Online MPC and mp-MPC results match.

## Slide 21
Conclusions and Future Work
Understanding of following algorithms:
  LP|LP BLPP problems.
  Multiparametric Linear Programming Problems (mp-LP)
  Multiparametric Quadratic Programming Problems (mp-QP)
Comfortable in solving online MPC and mp-MPC.
BLPP formulation for TClab.
Objective is to get better set point tracking subject to minimisation of manipulated variables (u1 and u2) in the inner level.
BLPP formulation for building system
Objective is to minimise pollution concentration subject to thermal comfort of the occupants.
The formulation is difficult as it involves non-linearity in its formulation.
After bilevel has been successfully deployed on TCLab we can extend that to understand complex systems.

## Slide 22
Acknowledgement
I am thankful to the Post-doc in our research group Dr. Radhe Saini for his guidance during my course project.
I am also thankful to Prof. Hari Ganesh research group
members for their support.
Thank You!