## Slide 1
Discipline of Chemical Engineering,
Indian Institute of Technology Gandhinagar,
Palaj, Gujarat – 382055
India
Model Predictive Control on an Arduino Device
10th Asian Symposium on Process Systems Engineering
Authors:
Subhi Gupta and Hari S. Ganesh

## Slide 2
Content
Introduction to Temperature Control Lab (TCLab)
System Modeling and Identification
Data Driven State Space Equations
Model Predictive Control
Parametric programming

## Slide 3
Temperature Control Lab (TCLab)
An application of feedback control with an Arduino, an LED, two heaters, and two temperature sensors.
A MIMO device for understanding the principles of modeling, estimation, and control.
Image Source Link: http://apmonitor.com/pdc/index.php/Main/ArduinoTemperatureControl
Introduction
Temperature sensors and heater transistors with connections to an Arduino Leonardo.
Temperature Sensors
Heaters
Epoxy

## Slide 4
Temperature Control Lab (TCLab)
.
Working Principle
PC
MATLAB/SIMULINK
ARDUINO UNO
POWER SUPPLY DC
HEATER
TIP41C
TEMPERATURE SENSOR (LM35)
Analog
Signal
PWM
(0-100%)
.
Reference: Application of different control algorithms on a ‘home-made’ temperature control lab kit.
Reference: https://apmonitor.com/pdc/index.php/Main/TCLabSensor
Reference: The basics of Arduino: Reading Voltage- Device Plus
Microcontroller board for hardware and software communication.
Implementation of control algorithm
Analog output control
Data Acquisition (conversion of analog signal to a digital signal to be understood by software)

## Slide 5
System Modeling and Identification
Dual Heater Modeling of TCLab (MIMO System)
Two energy balance equations that describe the dynamic temperature response
Reference link: apmonitor.com/do (John D. Hedengren)

## Slide 6
Data Driven State Space Equations
Step Response Analysis
Steady-state achieved for Q1=30 and Q2=30
Steady-state achieved for Q1=30 and Q2=30

## Slide 7
Data Driven State Space Equations
Step Response Analysis
Temperature simulation for step changes in Q1 and Q2
The above step response was used to develop data-driven state-space equations using the System Identification Toolbox.

## Slide 8
Data-Driven State Space Equations
The data obtained from the Step Response Analysis method represented a relationship between input/output.
The data is fed to MATLAB System Identification Toolbox and the differential equations representing the physical system were linearised.
The resulting pseudo states equations obtained in matrix form were used as linear constraints in MPC formulation.
State space equations were obtained from
MATLAB System Identification Toolbox

## Slide 9
Model Predictive Control (MPC)
MPC formulation is first reformulated into quadratic form using ss2qp_yalmip.
At each sampling instant the quadratic problem is solved using cplexqp solver.
quadprog can also be used but cplexqp gives more stable results.
State space equations
Formulation

## Slide 10
Closed-loop Simulation results.
Demonstration of Online MPC Control Calculations
Best Case of Tuning Parameters
Online MPC is computationally complex. There is low throughput
and high memory usage.
Next Task
Explicit MPC: MPC formulation was solved multi-parametrically (mp-MPC).

## Slide 11
Parametric Programming
Takes into account varying parameters (𝜃).
Approach is to obtain the optimal solution (𝒙) as an explicit function of the parameters.
General parametric nonlinear programming problem
An Effective Solution Strategy
Reference: Faísca NP, Dua V, Pistikopoulos EN. 2007 Feb 9;1:1-23.
Image Source: https://parametric.tamu.edu/POP/

## Slide 12
Multiparametric Programming
Formulation of Multiparametric Linear (mp-LP) and Quadratic Programming (mp-QP)
The parameter space(𝜃 ) is partitioned into nine set of critical regions (CRi).
Each critical region has its own function optimal solution x*(𝜃 ) and Z*(𝜃 )
Verification was done using quadprog solver
Solution of mp-QP: 𝒙(𝜃)𝘪=𝑊𝘪𝜃 + 𝘸 CR𝘪: Φ𝘪𝜃≤𝜙𝘪
Reference: Faísca NP, Dua V, Pistikopoulos EN. 2007 Feb 9;1:1-23.

## Slide 13
Explicit MPC
Solves the optimization problem offline for all the states within a range.
Solution is precomputed for each state within a range.
Advantages
u(x)
x

## Slide 14
Closed Loop Simulation Results
Online MPC
mp-MPC
Online MPC and mp-MPC results match.

## Slide 15
Hierarchical order in process industry
Background
Process control activities are organized in the form of hierarchy as shown in Figure 1.
For profitable plant operation the process control activities at different levels should be carefully coordinated.
Multi-level decision structures can be mathematically represented using multi-level programming principles.
Reference: Seborg DE, Edgar TF, Mellichamp DA, Doyle III FJ.2016 Sep 13.
Figure 1: Hierarchy of process control activities
To measure process variables and implement the calculated control actions.
Standard feedback and feedforward control techniques.
Model predictive control (MPC) strategy.

## Slide 16
Bilevel Programming Problem (BLPP)
In some literature, researchers have addressed bilevel decision-making problems.
Ryu et.al have taken one level as plant planning/control problem and other level as as distribution network problem.
Styliani et.al have recasted planning and scheduling integration as a bi-level multi-follower problem. Upper level (planning) and lower level (scheduling).
Bilevel programming have evolved significantly in recent years.
Tri-level and other general multi-level programming problems
too are evolving gradually.
Reference: Ryu JH, Dua V, Pistikopoulos EN. 2004 Jun 15;28(6-7):1121-9.
Reference: Avraamidou, S., & Pistikopoulos, E. N. (2018, June). IEEE.
Motivation

## Slide 17
Bilevel Programming Problem (BLPP)
Bilevel Optimization Model
Reference: Ryu JH, Dua V, Pistikopoulos EN. 2004 Jun 15
Leader’s problem or
High level decision problem
Follower’s problem or
Low level decision problem
First level (production model) is constrained by another optimization problem (second level,the distribution model).
Process configuration of an enterprise
Aim is to minimise both Production cost and distribution cost.

## Slide 18
Bilevel Programming Problem (BLPP)
Formulation of Linear BLPP (LP/BLPP)
Inner Level solved multi-parametrically
Reference: Faísca, Nuno P., et al. Journal of Global Optimization 38.4 (2007).
Five critical regions are obtained with y as an explicit function of x.

## Slide 19
Bilevel Programming Problem (BLPP)
Solution of a linear bilevel programming problem.
Solution obtained after solving outer level problem
Fields | Optimised variables (𝑥) | Function values
1 | [0.5000 ; 0.5000] | -6
2 | [0.5000 ; 0.5000] | -6.0000
3 | [0 ; 0.7500] | -23.0000
4 | [0.5000 ; 0.5000] | -6.0000
5 | [0 ; 0.9000] | -26
Global optimum solution

## Slide 20
Bilevel Model predictive control
One of the application of Bilevel lies in hierarchical model Predictive control (MPC) structures.
In recent attempt has been made to solve MPC in hierarchical manner.
Styliani et.al in 2017 employed two level hierarchical mp-MPC on a continuous stirred tank reactor (CSTR) system.
Use of a multi-parametric bi-level algorithm for the development of explicit hierarchical controllers has limited application.
So such algorithms hold a good possibility to be explored and extended on more complex systems in near future.
Controller 1 (Optimisation Problem 1)
Controller 2 (Optimisation Problem 2)
System
Avraamidou S, Pistikopoulos EN.In Computer aided chemical engineering 2017 Jan 1.Elsevier.

## Slide 21
Bilevel Model predictive control
Case Study

## Slide 22
Conclusions and Future Work

## Slide 23
Acknowledgement
I am thankful to the Post-doc in our research group Dr. Radhe Saini for his guidance during my course project.
I am also thankful to Prof. Hari Ganesh research group
members for their support.
Thank You!